## Slide 1
ROS Recap
From zero to a functional communication scheme

## Slide 2: ROS basics What is ROS ?
“ROS is an open-source framework that helps researchers and developers build and reuse code between robotics applications”

## Slide 3: ROS basics The conceptual idea behind ROS
University
/ROS
Teacher 1
Student A
Student B
/ROS
/Control
Teacher 2
Student D
Student C
/Control
/Weekend
/Party

## Slide 4: ROS basics What is the information delivered?
Any class has a certain format, which both the teacher and the student know off and is expected to be followed.
Between two friends you are not expecting a power point presentation but some plain text.
Teacher
Students
Presentation and a
practical explanation
Student
Student
Plain text and memes
/ROS
/Weekend
Publishers
Data types
Subscribers

## Slide 5: ROS Architecture ROS Master
Brain of ROS -> Process manager that enables the communication between different agents in the network.
Allows communication between different computers or robots by means of a Server – Client architecture
ROS Serial
TCP IP Com
ROS Master
User
Node 1
User
Node 2
Robot
Node
Micro.
Node

## Slide 6: ROS Architecture nodes and topics
Piece of software that acts as an element in the network.
It is in charge of executing a part of the code and can be programmed in Cpp, Python or Lisp.
Each topic has a unique msg type.
Node
White line detection
node
Obstacle detection
node
Hardware
Node
Get
data
/Image
Cables
Node

## Slide 7: ROS Architecture Services and actions
While topics are one way communication, services and actions allow feedback and prevent unnecessary load in the network.
Services follow a question-answer structure, while actions are designed to execute a task and give feedback during the process.
Planning Node
Control Node
Can you send me a path ?
Updated path
Service
Control Node
User Input Node
Move to point A
Success !
Action
Updates:
Current pose

## Slide 8: ROS Architecture A practical example
PC

## Slide 9: ROS Architecture Overview
Ros Master
Physical System
ROS Implementation
Control
Node
User
Node
Sensors
Node
Actuators
Node
Micro

## Slide 10: ROS Code Talker and listener framework
Simplest communication scheme.

## Slide 11: ROS Code Talker
#!/usr/bin/env python import rospy from std_msgs.msg import String
if __name__ == '__main__': pub = rospy.Publisher("chatter", String, queue_size=10) rospy.init_node("talker") rate = rospy.Rate(10)
while not rospy.is_shutdown(): hello_str = "hello world %s" % rospy.get_time() pub.publish(hello_str)
rate.sleep()
Terminal Commands
  roscore
  rosrun basic_comms talker.py
  rostopic echo /chatter
Setup environment and import libraries
Create variables and setup node
Publish message
Wait to run again

## Slide 12: ROS Code Listener
#!/usr/bin/env python import rospy from std_msgs.msg import String
def callback(msg): rospy.loginfo("I heard %s", msg.data)
if __name__ == '__main__': rospy.init_node('listener') rospy.Subscriber("chatter", String, callback)
rospy.spin()
Terminal Commands
  roscore
  rosrun basic_comms listener.py
  rostopic pub /chatter <tab complete>
Setup environment and import libraries
Define Callback
Create variables and initialise node
Continuously check for new messages

## Slide 13: ROS Tools ROS Terminal tools
roscore
  Must be executed before working with ros
  Handles the correct functionality of the network
rostopic
  Contains useful tools related with topics
  rostopic echo [topic name]
  rostopic list
  rostopic hz [topic name]
rosrun
  Executes a given node
  rosrun [package] [node name]
rosnode
  Contains useful tools related with nodes
  rosnode list
  rostopic info [node]

## Slide 14: ROS Tools ROS File structure
ROS projects are organized using workspaces, which are a collection of grouped codes called packages.
Instructions for the compiler need to be allocated in .cmake and package files
Package files are exportable between projects
Configuration files used to stablish code dependencies
Code that we will execute
Catkin_make will generate ‘src’ and ‘devel’ for you when compiling the workspace

## Slide 15: ROS Tools ROS Compilation tools
ROS requires to compile each package, generating dependencies related with other packages, external libraries or custom messages, services and actions.
The preferred compilation tool is known as catkin and uses two separated files, package.xml and CMakeLists.txt.
A useful command to create packages is:
  catkin_create_pkg [name] [list of dependencies]
Which generates an empty package and templates of both CMakeLists and package files.
More information about the syntaxis of this files can be found In http://wiki.ros.org/ROS/Tutorials/CreatingPackage
Projects are compiled with the instruction catkin_make and the instruction source [project]/devel/setup.bash needs to be executed to load the changes.

## Slide 16: Activity Moving a real PuzzleBot
Straight line
Square
Drive the robot in a straight line.
Drive the robot making a square with a side length of 1m.

## Slide 17: Activity SSH File transfer
You can directly add the jetson to you file System by following the next steps
  Connect to the puzzlebot WiFi network
  Go to files -> new location
  Type ssh://puzzlebot@10.42.0.1 and introduce the password
  Right click over the puzzlebot folder and select “add bookmark”
Now everytime you connect to the jetson network you´ll be able to acces files as they were in your computer.

## Slide 18: Activity Moving a real PuzzleBot
Copy your “puzzlebot” package inside the folder catkin_ws In the jetson root directory
Run the node in the jeson using ssh.
Copy your “puzzlebot” package inside the folder catkin_ws In the jetson root directory
Stablish a ros wifi communication and run the node in your computer.
Using ssh
Using ROS