## Slide 1
Control Systems in ROS
Puzzlebot Model
ROS tips and tricks

## Slide 2: The Task
Robot Position
Target Position

## Slide 3: The Control System
Plant
Controller
Sensors
Output
Set Point
Control Signal
Measured
Output
Error
+
-

## Slide 4: The Control System
Puzzlebot
Controller
Sensors
Robot Motion
Set Point
Control Signal
Measured
Output
Error
+
-

## Slide 5: Determining the Robot Position

## Slide 6: Determining the Robot Position

## Slide 7: Determining the Robot Position

## Slide 8: Determining the Robot Position

## Slide 9: Determining the Robot Position
Robot Location:
Pose of the robot at timestep (m, m, rad). Stored in memory, initial value 0
Robot Constants:
Wheel radius = 0.05 m
Distance between robot wheels = 0.19 m
Measured variables
( Wheel velocity (rad/s)
Time between samples (s)
Values of must be contained within a single circle:
Either:
Or:

## Slide 10: Activity
Implement a ROS node that computes the robot location using the encoder data
  It should subscribe to /wl and /wr, and publish the data to a suitable set of topics
  The published messages could be a set floats, or you can combine them in any way you see fit

## Slide 11: The Control System
PuzzleBot
Controller
Sensors
Robot Motion
Set Point
Control Signal
Measured
Output
Error
+
-
PuzzleBot
Controller
Encoders
Robot Motion
Set Point
Control Signal
Error
+
-

## Slide 12: The Error
Robot Position
Target Position

## Slide 13: atan2
The atan2 function is a special form of arctan or
It takes two arguments, and , and returns the angle to the axis:
It is included in most maths libraries, but it is recommended to use numpy, as numpy will be necessary later on in the course
import numpy
theta = numpy.arctan2(y,x)

## Slide 14: Activity
Modify the previous node to publish ed and etheta.
Set a target, and drive the robot around, checking that the angle to the target and the distance from the target are updated correctly
Remember to wrap all angles to within 1 circle

## Slide 15: The Control System
PuzzleBot
Controller
Encoders
Robot Motion
Set Point
Control Signal
Error
+
-
PuzzleBot
Controller
Encoders
Robot Motion
Control Signal
+
-

## Slide 16: The Controller
Since the robot is inherently stable, a simple PID scheme should be sufficient.
Start with a pair of proportional controllers:
… and add integral and derivative elements if necessary.

## Slide 17: ROS setup
Robot
Node
Controller
Node
/wl
/wr
/cmd_vel
Use wheel speeds to estimate robot position
Compute the error in distance and angle
Subscribe to wheel speeds on /wr and /wl
Apply PID controllers to get and
Publish and to /cmd_vel
Target Position

## Slide 18: /cmd_vel
Message type: Geometry Messages – Twist
Import command in python:
  from geometry_msgs.msg import Twist
6 fields accessed as follows:
  msg.linear.x, msg.linear.y, msg.linear.z
  msg.angular.x, msg.angular.y, msg.angular.z

## Slide 19: Tips and Tricks
Write and test your node with the PuzzleBot off the ground:
  Use this to check the basics of your code are working correctly, such as the sign (+/-) of your controller parameters and
  Does the robot turn towards the goal?
  Does the robot move towards or away from the goal?
Tune one of the controllers at a time. You may find it easier to tune first, while setting your robot to move with a fixed forward speed.
If in doubt, lower the value of the control constants.
You may find it helpful to use a launch file to load your controller constants in from a config.yaml file.

## Slide 20: Accuracy
It will not be possible to tune the controllers such that the robot moves perfectly into position.
  You will need a threshold after which your algorithm decides it has successfully arrived.
  Suggested initial threshold: 10 cm
Additionally, if you measure the position of the robot, it will likely not match up with the measurement computed from the encoders.
  This is inevitable due to additive noise in the encoder readings.
  The solution to this is to use sensors that can measure the position of the robot relative to its environment.

## Slide 21: ROS Tools ROS Launch Syntax
Launch files are sets of commands written in xml that allow executing various scripts at the same time.
The general syntaxis is the following
  <?xml version=“1.0”?>
  <launch>
  [Body of the launchfile]
  </launch>
This syntaxis allows to run any object used within the ROS architecture and has a wide variety of tools that allow to parametrize the launch file so that it can be adapted to the requirements of you project.
An extensive documentation can be found in http://wiki.ros.org/roslaunch

## Slide 22: ROS Tools ROS Launch code tools
Running a node
  <node name=“listener” pkg=“basic_comms” type=“listener.py” output=“screen”/>
Running another file or launch file
  <include file="$(dirname)/other.launch" />
Set parameters
  <param name="publish_frequency" type="double" value="10.0" />
Pass args to the launch file
  <arg name=”camera_id" value=”cam_3" />
Load files into the system
  <rosparam command="load" file="$(find package_name)/config/file_name.yaml" />

## Slide 23: The Task
Robot Position
Target Position